## Slide 1: Identifying Wafer Failures with Deep Learning
Ong Boon Ping A0195172B
Tan Chin Gee A0195296M
Han Dongchou Francis A0195414A
A CA2 Project by

## Slide 2: Description
In wafer probe testing, VDD resistance is measured. The VDD resistance is an indication of the quality of the memory chip.
The test results not only sorts out problematic or failing components, but they also help us understand whether the wafer fabrication processes have any issues.
To find out whether the fabrication processes have any problems, we measure the resistance distribution across the wafer. This can help to identify the source of the problem (whether it’s the wafer preparation, or grinding, or cutting).

## Slide 3: Complication
Wafer sawing (cutting) and grinding issues usually involve components around the wafer edge while dielectric (material) related problems can be taking place in any region around the center of the wafer.
Wafer sawing issues usually happen around an edge of the wafer with a unique orientation but wafer grinding poses problem around a larger area at the wafer edge.
The processes mentioned may lead to certain faults on the wafer and a specific process would create a fault with a pattern that is unique to it.

## Slide 4: Types of Wafer Problems

## Slide 5: Types of Wafer Problems
As discussed, wafer problems show up as identifiable patterns. From the wafer images, we could see that each type of wafer problem has a certain unique pattern. As a recap, there are 3 distinct problems related to wafer processes. Wafer Grinding, Wafer Saw and Dielectric.
Apart from the 3 distinct problems, we have 5 combinations of the distinct problems. For example, Grinding-Dielectric and Saw-Grinding.
Currently, it is through manual inspection that wafer problems are identified. For example, if the problem is due to Wafer Grinding, the pattern is at the edges with a certain orientation.
Dielectric (Material) problems manifest themselves in a certain pattern clustered towards the center of the wafer.
Wafer Saw problems appear at the edges too but with a different orientation to the Wafer Grinding related pattern.
We could have a combination of the aforesaid problems too, and these problems show up as a combination of the corresponding patterns.

## Slide 6: Application of Deep Learning
In this project, we apply deep learning neural network on wafer maps with simulated faults.
The faults are classified into 8 classes and the neural network was trained to recognize them.
Being able to recognize a particular wafer problem using Deep Learning means that we could automate the identification of wafer testing, and reduce the time to sort out the bad wafers. Most importantly we could pin-point a specific issue with a particular upstream process and to rectify it.

## Slide 7: Data Generation
A data set was generated which reflects the outcome from a typical wafer metrology process. The data points are resistance measurements (in ohm) on each wafer. On each wafer, there are 441 locations (21x21) to be processed by the neural network. The generated data set contains test results from 1090 wafers.
21
21
21 x 21 = 441 data points

## Slide 8: Data Generation
The 1090 wafer test results are put together based on:
  Those with saw cut defects. Pure saw cut defects would cover 5-45 degrees of the wafer edge location.
  Those with grind defects. Grind defects would cover 30-180 degrees of wafer edges. The dataset covers all cases where the center of grind defects are at 0,45,90,135,180,225,270,315 degrees on the wafer.
  Those with dielectric defects. These are usually found at the center of the wafer. Severe dielectric issue causes the radius of affected area to be increased. The dataset covers the different radii of defect areas.
The dataset also covers normal wafer test cases with random defects.

## Slide 9: Data Generation
For each data point, the range of the value is in between 0 and 500 ohm. The values which are close to 0 indicate that the corresponding data points are fault-free. Another way to look at this is that the semiconductor devices are conductive to electric currents with minimal resistance (small ohms). Those data points with failures show up with high resistance, up to 500 ohms.
The data points with high resistance form a certain pattern. The pattern correspond to a particular wafer problem, be it “Grind”, “Saw”, “Material”, or a combination of them.
Using Pattern Recognition, we could identify the specific problem that a wafer may have. Using Deep Learning, we could train a neural network to learn all the fault patterns so that it could recognize a particular problem with good accuracy.

## Slide 10: Data Generation
A typical data set contains test results from the wafers. These test results are gathered and stored in excel file along with manual classification by the technician.
The technician classifies specify whether it is “Grind”,”Saw” or “Material” issue or combination based on manual inspection of the wafers. Hence, there will be 3 columns.
In our application, there are a total of 8 classes that the neural network will sort the problems into.
Our data set is of the exact format of the actual wafer test results and manual classifications.

## Slide 11: Data Preparation
The data set containing test results on 1090 wafers were put together in an Excel file along with manual classifications.
The data set was split into train and test portions.
Each row in csv file represents 1 wafer and hence the need to reshape the raw data into 2D numpy array after test and train data split
raw_data = pd.read_excel('td6.xlsx',sheet_name = "td6") #raw data
sdarray=raw_data.drop(["saw","grind","dielectric"],axis=1) #Just the features. Drop the outputs
raw_label=raw_data.saw+2*raw_data.grind+4*raw_data.dielectric #The result. Combining 3 rows into value of 0 to 7
sdarray_train,sdarray_test,label_train,label_test = train_test_split(sdarray,raw_label,test_size = 0.2) #split test data
sdarray_train_np=sdarray_train.as_matrix() #Changing input format
twoDarray_train = sdarray_train_np.reshape((sdarray_train_np.shape[0], 21, 21)) # reshape data format to 2D
sdarray_test_np=sdarray_test.as_matrix()
twoDarray_test = sdarray_test_np.reshape((sdarray_test_np.shape[0], 21, 21)) # reshape data format to 2D
trDat=twoDarray_train
trLbl=label_train
tsDat=twoDarray_test
tsLbl=label_test
trDat = trDat.astype('float32')/500 #Convert ohm value to 1
tsDat = tsDat.astype('float32')/500 #

## Slide 12: Data Preparation
The input was converted to categorical value.
Number of classes is also accounted.
# Retrieve the row size of each image
# Retrieve the column size of each image
imgrows = trDat.shape[1]
imgclms = trDat.shape[2]
# reshape the data to be [samples][width][height][channel]
# This is required by Keras framework
trDat = trDat.reshape(trDat.shape[0],
imgrows,
imgclms,
1)
tsDat = tsDat.reshape(tsDat.shape[0],
imgrows,
imgclms,
1)
# Perform one hot encoding on the labels
# Retrieve the number of classes in this problem
trLbl = to_categorical(trLbl)
tsLbl = to_categorical(tsLbl)
num_classes = tsLbl.shape[1]

## Slide 13: Data Preparation
The input was converted to categorical value.
Number of classes is also accounted.
# Retrieve the row size of each image
# Retrieve the column size of each image
imgrows = trDat.shape[1]
imgclms = trDat.shape[2]
# reshape the data to be [samples][width][height][channel]
# This is required by Keras framework
trDat = trDat.reshape(trDat.shape[0],
imgrows,
imgclms,
1)
tsDat = tsDat.reshape(tsDat.shape[0],
imgrows,
imgclms,
1)
# Perform one hot encoding on the labels
# Retrieve the number of classes in this problem
trLbl = to_categorical(trLbl)
tsLbl = to_categorical(tsLbl)
num_classes = tsLbl.shape[1]

## Slide 14: Learning Rate Setting
Applying initial learning rate at the beginning, and applying step wise decay when setting the learning scheduler.

## Slide 15: Training the Neural Network – Standard Neural Network
We started with the standard convolutional neural network which gave us an accuracy of
91.74%
def createModel():
model = Sequential()
model.add(Conv2D(20, (5, 5), input_shape=(21, 21, 1), activation='relu'))
model.add(MaxPooling2D(pool_size=(2, 2)))
model.add(Conv2D(40, (5, 5), activation='relu'))
model.add(MaxPooling2D(pool_size=(2, 2)))
model.add(Dropout(0.2))
model.add(Flatten())
model.add(Dense(128, activation='relu'))
model.add(Dense(num_classes, activation='softmax'))
model.compile(loss='categorical_crossentropy', optimizer='adam', metrics=['accuracy'])
return model

## Slide 16: Results
Best accuracy (on testing dataset): 91.74%
Confusion Matrix
Original Convolutional Neural Network
Learning Rate = 2e^-3
Batch Size = 32
Loss value starts to increase…
Standard Neural Network

## Slide 17: Incorporating the Resnet
Input Layers
The input shape is (21,21,1)
16 Neurons of conv2D followed by batch normalization and RELU activation layer.
The output shape becomes (21,21,16)

## Slide 18: Residual Net Layer – resBlkV1
Consists of 3 blocks for each resBLKV1.
3 resBLKV1 are cascaded after input Residual layer.
After each residual layer, size of the image is reduced.
(21,21) -> (11,11)->(6,6)->(3,3)
After each residual layer, number of neurons increased.
16->32->64->128

## Slide 19: Incorporating the Resnet
Block 1
Block 2
Block 3

## Slide 20: Final Layers
The average pooling layers are used to average out the value from final image of (3,3) into just (1,1).
Flattened layer forms the final 1D layer.
Dense at output layer will give the final prediction value for the class.
In total, 1,392,864 parameters are used.

## Slide 21: Improved Results with Resnet – 1st Attempt
Best accuracy (on testing dataset): 97.71%
Confusion Matrix
Using Resnet layers
Learning Rate = 2e^-3
Batch Size = 32
HYPER-PARAMETERS

## Slide 22: Improved Results with Resnet – 2nd Attempt
Best accuracy (on testing dataset): 98.62%
Confusion Matrix
Using Resnet layers
Learning Rate = 1e^-3
Batch Size = 32
HYPER-PARAMETERS

## Slide 23: Improved Results with Resnet – Final Attempt
Best accuracy (on testing dataset): 99.08%
Confusion Matrix
Using Resnet layers
Learning Rate = 0.3e^-3
Batch Size = 30
HYPER-PARAMETERS

## Slide 24: Conclusion
This project enabled us to successfully apply pattern recognition techniques to identify the different types of wafer failures. Using the standard convolution algorithm, we are able to do the failure classification with a decent accuracy of 91.74%.
Successful Wafer Failure Identification
Accuracy is improved through the use of Resnet to increase the number of layers in the algorithm and tuning the parameters, achieving a final accuracy of 99.08%.
Pursuit of Higher Accuracy